## Slide 1
Data Available
Data​ | Collected From​ | Collected Till​ | Collection Frequency​ | % Missing data​
DCS BA_106 | 06-01-2021 | 30/10/2021​ | Hourly basis | NA ​
DCS Additional BA_106 | 06-01-2021 | 30/10/2021​ | Hourly basis | NA
Dimensions of the available dataset – The dataset has 12384 samples/records and 71 features/variables

## Slide 2
Active Run Data Availability
Based on the Naphtha Feed availability, active run state of the furnace is decided. In the sample space where feed availability is nearly zero, considered as offline state of the furnace.
Data | Available From | Available Till | Frequency | Treatment Performed
DCS BA_106 | 06-01-2021 | 02-05-2022 | Hourly Basis | Samples/ Records having naphtha feed as nearly zero are dropped from the sample space.
DCS Additional BA_106 | 06-01-2021 | 02-05-2022 | Hourly Basis | 
NOTE: Now the sample space is not continuous time series data as offline records are dropped.
Dimensions of the available dataset – The dataset has 11553 samples/records and 71 features/variables

## Slide 3
Historical Furnace Run Length Analysis
The sample space is consist of 15 active run information. Average run length for the historical samples is 32 days.
Chart: Historical Run Duration
| Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Run 6 | Run 7 | Run 8 | Run 9 | Run 10 | Run 11 | Run 12 | Run 13 | Run 14 | Run 15
RunDurationDays | 29.2083 | 37.25 | 41.9583 | 41.6667 | 42.375 | 32.25 | 33.25 | 20.5833 | 42 | 39.375 | 27.9583 | 26.5417 | 13.6667 | 28.3333 | 24.9583

## Slide 4
New Feature/Variable Creation
Our primary concern is to predict the furnace run length. In other words, how long the furnace is going to run from today.
Since, we had no direct information about the furnace run length in the sample dataset, we have derived relative run length for each cycle until the furnace is taken in offline mode.
The new feature is introduced as ‘Run Length’ in the feature space.
E.g. if total run length of one cycle is 40 and today the furnace is running on 5th day, the relative run length will be 35 days.

## Slide 5
Feature Space Correlation Analysis
Correlations computation and further treatment are carried out for the following features
Naphtha Feed from Coil 1 to 6 and Total Naphtha Feed
COT from Coil 1 to 6 and Average COT
CIT from Coil 1 to 6 and Average CIT
Dilution Steam Ratio from Coil 1 to 6 and Total Dilution Steam Ratio
CIP from coil 1 to 6 and Maximum CIP
Feed Temp 1 and 2