## Slide 1
Data Available
Data​ | Collected From​ | Collected Till​ | Collection Frequency​ | % Missing data​
DCS BA_106 | 06-01-2021 | 30/10/2021​ | Hourly basis | NA ​
DCS Additional BA_106 | 06-01-2021 | 30/10/2021​ | Hourly basis | NA
Dimensions of the available dataset – The dataset has 12384 samples/records and 71 features/variables

## Slide 2
Active Run Data Availability
Based on the Naphtha Feed availability, active run state of the furnace is decided. In the sample space where feed availability is nearly zero, considered as offline state of the furnace.
Data | Available From | Available Till | Frequency | Treatment Performed
DCS BA_106 | 06-01-2021 | 02-05-2022 | Hourly Basis | Samples/ Records having naphtha feed as nearly zero are dropped from the sample space.
DCS Additional BA_106 | 06-01-2021 | 02-05-2022 | Hourly Basis | 
NOTE: Now the sample space is not continuous time series data as offline records are dropped.
Dimensions of the available dataset – The dataset has 11553 samples/records and 71 features/variables

## Slide 3
Historical Furnace Run Length Analysis
The sample space is consist of 15 active run information. Average run length for the historical samples is 32 days.
Chart: Historical Run Duration
| Run 1 | Run 2 | Run 3 | Run 4 | Run 5 | Run 6 | Run 7 | Run 8 | Run 9 | Run 10 | Run 11 | Run 12 | Run 13 | Run 14 | Run 15
RunDurationDays | 29.2083 | 37.25 | 41.9583 | 41.6667 | 42.375 | 32.25 | 33.25 | 20.5833 | 42 | 39.375 | 27.9583 | 26.5417 | 13.6667 | 28.3333 | 24.9583

## Slide 4
TMT Data Analysis
Parameters | Missing records | % | Treatment Done
TMT Coil 1 | 96 | 0.08 | Since, TMT samples are collected on daily basis while the state of the furnace is online where as DCS samples are stored in hourly format. Hence TMT is converted in the hourly format. Which leads to the increase in missing values. Mean or median could be used to fill the missing values which might decrease the accuracy. Therefore, linear regression technique is used to fill those missing values.
TMT Coil 2 | 96 | 0.08 | 
TMT Coil 3 | 96 | 0.08 | 
TMT Coil 4 | 96 | 0.08 | 
TMT Coil 5 | 96 | 0.08 | 
TMT Coil 6 | 96 | 0.08 | 

## Slide 6
New Feature/Variable Creation
Our primary concern is to predict the furnace run length. In other words, how long the furnace is going to run from today.
Since, we had no direct information about the furnace run length in the sample dataset, we have derived relative run length for each cycle until the furnace is taken in offline mode.
The new feature is introduced as ‘Run Length’ in the feature space.
E.g. if total run length of one cycle is 40 and today the furnace is running on 5th day, the relative run length will be 35 days.

## Slide 7
Feature Space Correlation Analysis
Correlations computation and further treatment are carried out for the following features
Naphtha Feed from Coil 1 to 6 and Total Naphtha Feed
COT from Coil 1 to 6 and Average COT
CIT from Coil 1 to 6 and Average CIT
Dilution Steam Ratio from Coil 1 to 6 and Total Dilution Steam Ratio
CIP from coil 1 to 6 and Maximum CIP
Feed Temp 1 and 2

## Slide 8
Naphtha Feed Correlation Analysis
Chart: Naphtha Feed Correlation Plot
| NpahthaFeedCoil1 | NpahthaFeedCoil2 | NpahthaFeedCoil3 | NpahthaFeedCoil4 | NpahthaFeedCoil5 | NpahthaFeedCoil6 | Total_Naphtha_Feed
Series 1 | 0.97614 | 0.97614 | 0.97505 | 0.95482 | 0.95817 | 0.9232 | 1
The sample dataset is having 6 columns (individual Naphtha Feed coils). Each columns are highly correlated to each other.
Treatment:
  Total Naphtha Feed is computed across all the columns.
  Since Total Naphtha Feed is highly correlated with all individual columns. Hence individual Naphtha Feed columns are dropped and replaced with Total Naphtha Feed.

## Slide 9
COT Correlation Analysis
Chart: COT Correlation Plot
| COT1 | COT2 | COT3 | COT4 | COT5 | COT6 | Avg_COT
Avg_COT | 0.99538 | 0.99267 | 0.99778 | 0.99397 | 0.99443 | 0.99517 | 1
The sample dataset consists of 6 columns (individual COT coils). Each columns are highly correlated to each other.
Treatment:
  Average COT is computed across all the columns.
  Since Average COT is highly correlated with all individual columns. Hence individual COT columns are dropped and replaced with Average COT.

## Slide 10
Dilution Steam Ratio Correlation Analysis
Chart: DS Ratio Correlation Plot
| DSRatioCoil1 | DSRatioCoil2 | DSRatioCoil3 | DSRatioCoil4 | DSRatioCoil5 | DSRatioCoil6 | Total_Ds_Ratio
Total_Ds_Ratio | 0.97918 | 0.97453 | 0.9861 | 0.96777 | 0.9741 | 0.96102 | 1
The sample dataset consists of 6 columns (individual Dilution Steam coils). Each columns are highly correlated to each other.
Treatment:
  Total DS Ratio is computed across all the columns.
  Since Total DS Ratio is highly correlated with all individual columns. Hence individual DS Ratio columns are dropped and replaced with Total DS Ratio.

## Slide 11
Cross Over Temperature Correlation Analysis
Chart: CIT Correlation Plot
| CrossOverTemp_Coil1 | CrossOverTemp_Coil2 | CrossOverTemp_Coil3 | CrossOverTemp_Coil4 | CrossOverTemp_Coil5 | CrossOverTemp_Coil6 | Avg_CIT
Avg_CIT | 0.91055 | 0.96757 | 0.91635 | 0.93406 | 0.94388 | 0.91507 | 1
The sample dataset consists of 6 columns (individual CIT coils). Each columns are highly correlated to each other.
Treatment:
  Average Cross Over Temperature is computed across all the columns.
  Since Average Cross Over Temperature is highly correlated with all individual columns. Hence individual CIT columns are dropped and replaced with Average Cross Over Temperature.

## Slide 12
Coil Inlet Pressure Correlation Analysis
Chart: CIP Correlation Plot
| CIP1 | CIP2 | CIP3 | CIP4 | CIP5 | CIP6 | Max_CIP
Max_CIP | 0.82785 | 0.87425 | 0.96832 | 0.81365 | 0.77956 | 0.92365 | 1
The sample dataset consists of 6 columns (individual CIP coils). Though not all the columns are highly correlated to each other, they are having correlation value greater than 0.75. This implies those individual column samples contain similar information.
Treatment:
  Maximum CIP is computed across all the columns.
  Since maximum CIP is highly correlated with all individual columns. Hence individual CIP columns are dropped and replaced with Average Cross Over Temperature.